## Slide 1: Architectural Modeling and Analysis for Safety Engineering (AMASE)
Danielle Stewart
Oral Preliminary Exam
January 2019
  Model-based safety analysis of critical systems

## Slide 2: Motivation
Requirements and
Design Documents
Safety
Analyst A
Safety
Analyst B
System Safety Analysis is
- Based on Informal Specifications
- Highly Dependent on Skill of the Analyst
Adapted from Stephen Miller
Notes: Safety engineers do most of the analysis activities like fault tree creation manually, based on a lot of informal requirements and design documents. These analyses seem to be quite subjective and highly dependent on the skill and experience of the safety engineers. Thus, it is not surprising that different safety engineers will quite often produce fault trees, which may differ in substantial ways. It is only through a rigorous review process that a concensus will be built on the correct fault tree, which captures the right fault behavior. We think that the review process implicitly consolidates existing information from various documents and then completes it with unspecified details architectural and fault behaviors. It would be great if all these activities would be based off a comprehensive system architecture.
We also observe that due to the complexity of the systems involved, it is possible that the fault trees may not capture involved fault scenarios that may occur due to complex interactions between components.

## Slide 3: Model-Based Development
We Base the Entire
Development Cycle
Around the Model
Why Not the
Safety Analysis?
Adapted from Stephen Miller

## Slide 4: Model-Based Safety Analysis
Add Fault Model for Physical System
Power A
Pedal 1
Feed back
Plant
Fault Tolerant
Control Unit
( BSCU )
Braking System
System
A
Power B
Pedal 2
System
B
Plant
Model
AntiSkid
Command
Braking
+
AntiSkid
Command
Green Pump
Blue Pump
Isolation Valve
Isolation Valve
Shut
Normal
System
N
O
R
M
A
L
A
L
T
E
R
N
A
T
E
Accumulator
Pump
Meter
Valve
Meter
Valve
Meter
Valve
Accumulator
Valve
Mechanical
Pedal
Selector Valve
Model the Digital Controller Architecture
Automation Enables “What-If” Consideration of System Designs
and Digital Controller Architecture
Integrates System and Safety Engineering About a Common Model
and the Physical System
Wheel Braking System
AIR6110
CONTIGUOUS AIRCRAFT/SYSTEM DEVELOPMENT PROCESS EXAMPLE
Adapted from Stephen Miller
Notes: Steve’s slide

## Slide 5: Fault and Failure Definitions
Fault: something can go wrong. When that happens, we have a
Failure: The corrupted state of the component is observable.
A failure may only be observable on a component level. It may or may not lead to a top level system failure.
This failure state can be propagated from the component to other components and may propagate to the top level of the system.

## Slide 6: Conceptions of MBSA
Failure propagations:
Failure Logic Modeling (FLM)
Failure Effect Modeling (FEM)
Directional vs Bidirectional flows
Purpose Built Fault Model vs Extension of System Model
Compositional Analysis or Monolithic Analysis

## Slide 7: Existing Tools and Methods
 | FLM | FEM : Directional | FEM: Bidirectional | M | C | PB | ESM
EMV2 | ✓ |  |  |  |  |  | AADL
Compass | ✓ |  |  |  | ✓ |  | SLIM
SmartIFlow |  |  | ✓ | ✓ |  | ✓ | 
SAML |  | ✓ |  | ✓ |  | ✓ | 
AltaRica |  |  | ✓ | ✓ |  | ✓ | 
HipHops | ✓ |  |  |  |  |  | East-ADL

## Slide 8: Where does the our research fit?
Extend System Model
Compositional and Monolithic Analysis
Implicit and Explicit Failure Propagation (FEM and FLM)

## Slide 9: Existing Tools and Methods
 | FLM | FEM : Directional | FEM: Bidirectional | M | C | PB | ESM
EMV2 | ✓ |  |  |  |  |  | AADL
Compass | ✓ | ✓ |  |  | ✓ |  | SLIM
SmartIFlow |  |  | ✓ | ✓ |  | ✓ | 
SAML |  | ✓ |  | ✓ |  | ✓ | 
AltaRica |  |  | ✓ | ✓ |  | ✓ | 
HipHops | ✓ |  |  |  |  |  | East-ADL
Our Research | ✓ | ✓ |  | ✓ | ✓ |  | AADL

## Slide 10: Creation of Nominal System Model
Power A
Pedal 1
Feed back
Plant
Fault Tolerant
Control Unit
( BSCU )
Braking System
System
A
Power B
Pedal 2
System
B
Model of the Digital System
Plant
Model
AntiSkid
Command
Braking
+
AntiSkid
Command
Green Pump
Blue Pump
Isolation Valve
Isolation Valve
Shut
Normal
System
N
O
R
M
A
L
A
L
T
E
R
N
A
T
E
Accumulator
Pump
Meter
Valve
Meter
Valve
Meter
Valve
Accumulator
Valve
Mechanical
Pedal
Selector Valve
Power A
Pedal 1
Feed back
Plant
Fault Tolerant
Control Unit
( BSCU )
Braking System
Power B
Pedal 2
System
B
Model of the Digital System +
Model of the Mechanical System
Verify safety properties of the nominal digital system
Verify safety properties of the nominal mechanical system
Adapted from Stephen Miller

## Slide 11: Wheel Brake System

## Slide 12: Architecture Analysis and Design Language (AADL)
AADL = SAE AS5506 standard
Target: Embedded, real-time, distributed systems
Describes both hardware and software
Extensible syntax (annex)
Open source tools, supported by SEI
Slide from Collins Aerospace

## Slide 13: Architecture Modeling and Analysis Tools
Trusted
Build
Architecture Translation
seL4
eChronos
VxWorks
A
B
C
Assumption: Input < 20
Guarantee: Output < 2*Input
Assumption: Input < 20
Guarantee: Output < Input + 15
Assumption: none
Guarantee: Output = Input1 + Input2
Assumption: Input < 10
Guarantee: Output < 50
Architecture Analysis
Architecture Models
OSATE
Resolute
AGREE
SIM
Kind/JKind
Model Checker
TCG
Adapted from Collins Aerospace
Notes: START AGREE HERE

## Slide 14: WBS AADL Model

## Slide 16: AGREE: Assume Guarantee Reasoning Environment
Each component has a contract consisting of assumptions and guarantees
  Assumptions: Constraints over what a component expects from its environment
  Guarantees: Constraints over how a component behaves in response to its environment (requirements)
The contract of a component abstracts the behavior of its implementation
AGREE analysis
Component
Implementation
contract
contract
contract
contract
contract
contract
contract
Slide from Collins Aerospace

## Slide 17
Compositional verification tool for analysis of AADL system models
AGREE: Assume-Guarantee Reasoning Environment
Focus on system safety properties
Compositional approach scales model checking to larger systems
Compositional Verification of Critical Systems
A
B
C
Assumption: Input < 20
Guarantee: Output < 2*Input
Assumption: Input < 20
Guarantee: Output < Input + 15
Assumption: none
Guarantee: Output = Input1 + Input2
Assumption: Input < 10
Guarantee: Output < 50
FCC
FCC
FCC
FCC
DaC
DaC
DaC
DaC
AFDX or
TTE
Switch
AFDX or
TTE
Switch
Example system: Quad-redundant flight control system provided by NASA
Slide from Collins Aerospace

## Slide 18
Compositional verification tool for analysis of AADL system models
AGREE: Assume-Guarantee Reasoning Environment
Focus on system safety properties
Compositional approach scales model checking to larger systems
Compositional Verification of Critical Systems
FCC
FCC
FCC
FCC
DaC
DaC
DaC
DaC
AFDX or
TTE
Switch
AFDX or
TTE
Switch
Example system: Quad-redundant flight control system provided by NASA
Adapted from Collins Aerospace
A
B
C
Assumption: Input < 20
Guarantee: Output < 2*Input
Assumption: Input < 20
Guarantee: Output < Input + 15
Assumption: none
Guarantee: Output = Input1 + Input2
Assumption: Input < 10
Guarantee: Output < 50

## Slide 19
Nominal Model Component in AADL and AGREE
Notes: Maybe remove, check on other agree slides

## Slide 20
Wrap nominal component in fault
Watch behavior of system through AGREE contracts
Creation of the Fault Model

## Slide 21
Component A
Component B
Out
In
Component A
Component B
Out
In
Nominal Behavior:
Fault Behavior:
Fault

## Slide 22: WBS Top Level Property : No inadvertent braking
Nominal Behavior:
Mechanical pedal pressed (brakes commanded)
Sensor on pedal converts to electrical signal
Signal sent to BSCU to command brakes

## Slide 23: A Fault on the Pedal Sensor Component

## Slide 24: Active Sensor Fault
Mechanical pedal is not pressed
Inverted Boolean failure on sensor activated
Electrical signal is true and braking is commanded through BSCU
Top level lemma fails (Unintentional braking occurs)

## Slide 25: Probabilistic Analysis and Maximum Faults
. . .
. . .

## Slide 26
. . .
. . .
Probabilistic Analysis and Maximum Faults

## Slide 27: Probabilistic Analysis and Maximum Faults
. . .
. . .

## Slide 28: Probabilistic Analysis and Maximum Faults
. . .
. . .

## Slide 29: Current Support
Maximum number of faults in a given layer of the architecture
Probabilistic analysis
Hardware and software faults

## Slide 30: Future Work
Compositional Fault Tree Generation and Probabilistic Analysis
Allow for more flexible modeling:
  Byzantine Fault Modeling
  Transient Faults Analysis

## Slide 31: Motivation for Compositional Fault Analysis
Currently: Given top level threshold, do the fault combinations exceed it?
Desire: Given faults and probabilities, what is the threshold of the system?
Currently: Fault tree analysis done monolithically.
Desire: Generate informative Fault Trees containing both fault model information and nominal model architecture.

## Slide 32: Challenges and Lessons Learned
Theorizing an idea
The correct implementation of the theory
The correct order of theorizing and then implementing
The challenge of working with pre-existing tools and extending a language correctly
Staying up-to-date on new research in the field

## Slide 33: A special thank you to...
Darren Cofer, Janet Liu, and Mike Peterson from Collins Aerospace
Kurt Woodham from NASA
Mike Whalen from UMN/Amazon