## Slide 1: Using Inductive Validity Cores to Generate Minimal Cut Sets
University of Minnesota
Danielle Stewart

## Slide 2: Critical System Development
System Development
Safety Analysis

## Slide 3: Common Artifacts of the Safety Assessment Process
Fault Trees:
  The relationship between active faults and the hazard they cause.
  Usually reflects signal flows within the system.
Minimal cut sets:
  The minimal sets of faults that lead to a given hazard.
  The faults in the AND nodes of the fault tree.
Top Level Event

## Slide 4: Minimal Cut Sets
  Minimal sets of faults that violate safety property
  Commonly used as safety analysis artifact
  Gives information on critical faults in a system
  Often performed manually
  Automatic generation hindered by scalability issues
The main idea:
Automatic generation of minimal cut sets via proof information provided by model checker
MinCutSet 1:
MinCutSet 2:
Top Level Event

## Slide 5: MinCutSet Generation Issues
  Often generated manually
  Scalability issues with cyber-physical systems
  Can we automate the process?
  Can we provide a more scalable approach?

## Slide 6: Model Based Safety Analysis
We Base the Entire
Development Cycle
Around the Model
Why Not the
Safety Analysis?

## Slide 7
System Functional
Hazard Assessment (FHA)
System Safety
Assessment (SSA)
Fault Tree
Analysis (FTA)
Preliminary System Safety Assessment (PSSA)
Common Cause
Analyses (CCA)
Development of
System Architecture
Safety Assessment Process
System Development Process
Allocation of System
Requirements to
Hardware and Software
System Implementation
System Integration &
Verification
Shared
Model

## Slide 8: AADL and AGREE
AADL = SAE AS5506 standard
Target: Embedded, real-time, distributed systems
Describes both hardware and software
Extensible syntax (annex)
Open source tools
AGREE: Assume Guarantee Reasoning Environment
Behavioral model defining requirements for each system component.
Each component has a contract consisting of assumptions and guarantees
Allows for compositional or monolithic verification
Uses JKind model checker over AADL/AGREE model

## Slide 9: The Safety Annex for AADL
Define faults for components in a system
Use model checker to verify behavior of system in the presence of faults
See effects of active faults in the behavior of components through verification of AGREE contracts.
Guarantees on output
Assumptions on input
Component A
Component B
Out
In
F
If fault is active, it could violate guarantees of A and assumptions of B.
If fault is inactive, the output of A remains unchanged.
If the violated guarantee is used in the proof of the system safety property, it is seen in the fault analysis.

## Slide 10: Scalability: Monolithic vs. Compositional Verification
S
Monolithic: Use all contracts of the system to prove the top level property.
Compositional: Perform the analysis one layer at a time, from the top down.

## Slide 11: Hierarchical Layers of a System
S
S
A
B
D
C
F
E
System S
Prop:
Component A
Prop:
Comp C
Comp D
Comp E
Comp F
Component B
Prop:

## Slide 12: Compositional Verification
S
System S
Prop:
Component A
Prop:
Comp C
Comp D
Comp E
Comp F
Component B
Prop:
First layer of analysis:
Second layer of analysis:

## Slide 13: Problem with MinCutSets and Compositional Verification
S
System S
Prop:
Component A
Prop:
Comp C
Comp D
Comp E
Comp F
Component B
Prop:
First layer of analysis:
Second layer of analysis:
Is required to prove ?

## Slide 14: JKind Analysis and Constraint Systems
: Satisfiable
: Unsatisfiable

## Slide 15: Minimal Unsatisfiable Subsets (MUSs)

## Slide 16: Minimal Inductive Validity Cores (MIVCs)
  Given a constraint system, JKind‘s MIVC algorithm returns the minimal set of elements necessary to find proof of property P.
Model Checker
Ghassabani, E., Whalen, M.W., and Gacek, A. “Efficient generation of all minimal inductive validity cores” FMCAD, (2017)

## Slide 17: Minimal Inductive Validity Cores
  A requirement of the MIVC algorithm is that the safety property P proves given constraints, .
  The constraint system for the MIVC algorithm is:
  Given the assumption above, this constraint system is UNSAT
  MIVC algorithm finds the minimal UNSAT cores for the unsatisfiable constraint system.
  These are the minimal model elements needed to prove the property P.

## Slide 18: Minimal Correction Sets (MCSs)

## Slide 19: Duality of MUS and MCS: Minimal Hitting Sets
A hitting set of a collection of sets A is a set H such that every set in A is hit by H.
, {
One can find all MCSs by finding the Minimal Hitting Sets of all MUSs.

## Slide 20: What do MCSs have to do with safety?
If the constraints found in an MCS are removed from the constraint system, it becomes SAT.
Add all faults to the system and constrain them to false.
MUSs and MCSs will now contain fault information:
MCS now contains faults and if these fault constraints are removed from C, the system is SAT with respect to which is the Top Level Event.

## Slide 21: Example
System S
Prop:
Component A
Prop:
Component B
Prop:
Remove constraints from C found in MCS:
Faults occur; violates ; satisfies

## Slide 22: MCS to MinCutSet
Case 1:
MCS only contains fault literals
  → Remove constraints on faults
Case 2:
MCS contains faults and contracts
  → Replace contracts with faults that cause
  their violation
  → Remove constraints on faults

## Slide 23: The Main Idea
Constraint System
1. Add constrained faults
to constraint system
2. Get all MUSs from
All-MIVC algorithm
3. Get all MCSs from
Hitting Set Algorithm
4. Transform MCSs
Into MinCutSets
All MUSs
…

## Slide 24: Future Work
  Ongoing conversations with safety analysts to provide tools they need (and will use)
  Further integration of formal methods into both the system development and safety assessment processes
  Encouragement in industry to adopt a model based approach
  Look into further ways the proof information can be used to shed light on other aspects of system/safety (i.e., assurance cases, critical component detection, etc.)

## Slide 25
Questions
?

## Slide 26: Verification in the Face of Component Failures
Maximum no. of faults analysis threshold
Are contracts violated in the presence of n active faults?
Probabilistic analysis threshold
Are contracts violated with a probability greater than x?

## Slide 27: Flexible Fault Modeling
Behavioral Propagation
The effects of an active fault propagate through the system naturally
Explicit Propagation (dependencies)
Analyst explicitly states dependencies and propagations

## Slide 28: JKind Model Checker
Structured as parallel engines that coordinate to prove properties and perform other verification tasks
System and Behavioral Model
(.lus)
AGREE Parser
AADL type and
Implementation
annex agree{**
contracts
**};
AGREE Program
AADL System Model
(.aadl)
Abstract Syntax Tree
(.java)
JKind Program
(Lustre)
JKind

## Slide 29: Implementation of the Safety Annex
System and Behavioral Model
(.lus)
AGREE Parser
AADL type and
Implementation
annex agree{**
contracts
**};
annex safety{**
faults
**};
AGREE Program
AADL System Model
(.aadl)
Abstract Syntax Tree
(.java)
JKind Program
(Lustre)
JKind
AGREE Plugin
Safety Parser
Fault Model
Abstract Syntax Tree
(.java)
Safety Plugin
Extension
Point
AGREE AST with
fault
information

## Slide 30: Implementation
  Automatically insert defined faults into AGREE program as IVC elements for consideration. Set these equal to false.
  Run analysis on the model and request All-MIVCs from JKind.
    The analysis results are a tree reflecting at each layer the MIVCs pertaining to properties.
  Use Minimal Hitting Set Algorithm to find all Minimal Correction Sets per property.
  Transform the MCSs into MinCutSets.