## Slide 1: The Safety Annex for The Architecture Analysis and Design Language
Embedded Real Time Systems
January 2020
Danielle Stewart, Jing (Janet) Liu, Darren Cofer,
Mats Heimdahl, Michael Whalen, Michael Peterson

## Slide 2: Traditional safety assessment process Guidelines
ARP4761: Guidelines and Methods for Conducting the Safety Assessment Process on Civil Airborne Systems and Equipment
Provides Safety Guidelines and Methods
ARP4754A: Guidelines for Development of Civil Aircraft and Systems
ARP4754A provides guidance on applying development assurance at each hierarchical level throughout the development life cycle of highly-integrated/complex aircraft systems to establish the assurance process.
The safety assessment process is used to show compliance with certification requirements and for meeting a company’s internal safety standards.
ARP4761 identifies a systematic means to show compliance, including:
  Preliminary System Safety Assessment (PSSA) that evaluates the proposed system design and defines safety requirements
  System Safety Assessment (SSA) that evaluates the implemented system to show that safety requirements defined in the PSSA and certification regulation documentation are in fact satisfied.

## Slide 3: Traditional safety assessment process
Completeness of the traditional system safety analysis artifacts is subjective and dependent on the skill of the practitioner
Based on informal (or non-existent) system models that are incomplete, imprecise, possibly inconsistent
Architectural details about the system behavior gathered from multiple sources
Developing adequate understanding especially for software components is a difficult and time consuming endeavor

## Slide 4: MBSA process
Have system developers and safety engineers use the same system models created during a model-based development process
Extend system model to add capabilities for reasoning about faulty behaviors

## Slide 5: MBSA process Steps
Safety Engineers
System Engineers
Capture Design Information in a shared model (architecture, nominal behavior, system level safety requirements)
Check that safety requirements are satisfied by the nominal design model with the backend model checker
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults with the backend model checker, using counterexamples and fault trees produced for diagnosis
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design
Drive for design change
Starts
Ends

## Slide 6: What will help safety analysts do this?
Shared model
  Modeling language expressive enough to capture HW/SW, standard language
Flexible error propagations
  Behavioral AND explicit propagations
Flexible fault modeling
  Symmetric, asymmetric, dependent, independent
Backend model checker
  Used to assess design with or without active faults
Ability to generate assessment artifacts
  System traces, counterexamples, minimal cut sets, fault trees, etc.

## Slide 7: Closely Related work
EMV2:
  Model based, generates artifacts, captures propagations explicitly
COMPASS:
  Model based, generates artifacts, captures behavioral and explicit propagations, is not an SAE standard language: not as descriptive as AADL for real-time embedded systems

## Slide 8: MBSA process Steps
Safety Engineers
System Engineers
Capture Design Information in a shared model (architecture, nominal behavior, system level safety requirements)
Check that safety requirements are satisfied by the nominal design model with the backend model checker
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults with the backend model checker, using counterexamples and fault trees produced for diagnosis
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design
Drive for design change

## Slide 9: AADL
AADL = SAE AS5506 standard
Target: Embedded, real-time, distributed systems
Describes both hardware and software
Extensible syntax (annex)
Open source tools, supported by SEI

## Slide 10: Assume-Guarantee Reasoning Environment (AGREE)
Each component has a contract consisting of assumptions and guarantees
  Assumptions: Constraints over what a component expects from its environment
  Guarantees: Constraints over how a component behaves in response to its environment (requirements)
Component Implementation
AGREE
contract
contract
contract
Assumptions (input)
Guarantees (output)
A system with subcomponents

## Slide 11: MBSA process Steps
Safety Engineers
System Engineers
Capture Design Information in a shared AADL/AGREE model (architecture, nominal behavior, system level safety requirements)
Check that safety requirements are satisfied by the nominal design model with the backend model checker
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults with the backend model checker, using counterexamples and fault trees produced for diagnosis
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design
Drive for design change

## Slide 12: Wheel brake system (WBS)

## Slide 13: AADL and Agree
AGREE is incorporated as an annex of AADL

## Slide 14: Safety requirements for WBS

## Slide 15: MBSA process Steps
Safety Engineers
System Engineers
Capture Design Information in a shared AADL/AGREE model (architecture, nominal behavior, system level safety requirements)
Check that safety requirements are satisfied by the nominal design model with the backend model checker
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults with the backend model checker, using counterexamples and fault trees produced for diagnosis
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design
Drive for design change

## Slide 16: Nominal model analysis output

## Slide 17: MBSA process Steps
Safety Engineers
System Engineers
Capture Design Information in a shared AADL/AGREE model (architecture, nominal behavior, system level safety requirements)
Check that safety requirements are satisfied by the nominal design model with the backend model checker
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults with the backend model checker, using counterexamples and fault trees produced for diagnosis
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design
Drive for design change

## Slide 18: Nominal model analysis output
Safety syntax is incorporated as an annex of AADL

## Slide 19: Defining faults on component outputs
Valves
  Stuck open
  Stuck closed
  Stuck non-deterministically
Sensors
  Output inverted
Pumps
  Output zero
Calculating components and Gates
  Erroneous data

## Slide 20: A fault definition
Selector Valve
Blue pump in
Green pump in
Blue line out
(blue_select_out)
Green line out

## Slide 21: Behavioral error propagation
Wrap nominal component output in fault
Watch behavior of system through AGREE contracts when fault is activated
Component A
Component B
Out
In
Component A
Component B
Out
In
Nominal Behavior:
Fault Behavior:
Fault

## Slide 22: MBSA process Steps
Safety Engineers
System Engineers
Capture Design Information in a shared AADL/AGREE model (architecture, nominal behavior, system level safety requirements)
Check that safety requirements are satisfied by the nominal design model with the backend model checker
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults with the backend model checker, using counterexamples and fault trees produced for diagnosis
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design
Drive for design change

## Slide 23: Specify fault hypothesis statement
Specifies type of analysis to perform
Max N Analysis
Probabilistic Analysis

## Slide 24: MBSA process Steps
Safety Engineers
System Engineers
Capture Design Information in a shared AADL/AGREE model (architecture, nominal behavior, system level safety requirements)
Check that safety requirements are satisfied by the nominal design model with the backend model checker
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults with the backend model checker, using counterexamples and fault trees produced for diagnosis
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design
Drive for design change

## Slide 25: Fault Analysis results
Max 1 Fault Analysis for WBS

## Slide 26: Other Generated artifacts
Counterexamples showing trace of the system
Minimal cut sets
  Tally format
  Textual format
Fault Trees (with or without probabilistic information)
  Text format
  Graph format

## Slide 27: MBSA process Steps
Safety Engineers
System Engineers
Capture Design Information in a shared AADL/AGREE model (architecture, nominal behavior, system level safety requirements)
Check that safety requirements are satisfied by the nominal design model with the backend model checker
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults with the backend model checker, using counterexamples and fault trees produced for diagnosis
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design
Drive for design change

## Slide 28: Counterexample view
Max 1 Fault Analysis for WBS

## Slide 29: Assess behavior with faults
Pedal not pressed
Sensor reports that it was pressed
BSCU commands braking

## Slide 30: MBSA process Steps
Safety Engineers
System Engineers
Capture Design Information in a shared AADL/AGREE model (architecture, nominal behavior, system level safety requirements)
Check that safety requirements are satisfied by the nominal design model with the backend model checker
Augment the nominal model with the component failure modes
Specify the fault hypothesis for the analysis
Analyze if the safety requirements are satisfied by the design in the presence of faults with the backend model checker, using counterexamples and fault trees produced for diagnosis
Drive for design change
Examine the results to assess the validity of the fault combinations and the fault tolerance level of the system design

## Slide 31: Assess behavior with faults
Redundancy in the Pedal Sensor

## Slide 32: Results of Design Change
Now resilient to this single fault

## Slide 33: Future work
Use the information gleaned from the collection of minimal cut sets for interesting things:
  Use fault probabilities to calculate the system threshold
  Integrate into hierarchy of system to show more meaningful fault trees
Plans for use in a large scale aircraft system in 2020

## Slide 34: questions

## Slide 35: Example Safety Artifacts Generated
Fault Trees
Minimal Cut Sets
Text
Probabilities
Graph
List
Tally
Panagiotis Manolios, Kit Siu, Michael Noorman and Hongwei Liao. A Model-Based Framework for Analyzing the Safety of System Architectures. RAMS, the 65th Annual Reliability and Maintainability Symposium, 2019. http://www.ccs.neu.edu/home/pete/research/rams-2019.html